## Slide 1: Purification of Green Fluorescent Protein

## Slide 2: Biomanufacturing Steps in Product Purification
UPSTREAM PROCESSING
  Genetically engineered protein produced by an organism (ex. E.coli) are grown to yield the optimal amount of product
DOWNSTREAM PROCESSING
  Cells which do not export product need to be, isolated, homogenized, and crude fractions obtained by centrifugation
  Chromatography of partially purified product is then carried out

## Slide 3: Green Fluorescent Protein
Why we use GFP production to exemplify Biomanufacturing Process
Useful in following the purification process by using UV light detection of GFP
In the presence of arabinose, GFP gene is transcribed into mRNA and translated into protein product

## Slide 4: Flow Chart for GFP Product in Process
Production of GFP by Cell Growth and Division
Harvesting and Initial Purification
Chromatography and highly purified final product
Step 1
Growth of cells
Step 2
Crude separation of
product
3. Step
Purification by
Chromatography

## Slide 5: STEP 1 - Cell Growth of Transformed E.coli Results In GFP Product
Bio-rad.com

## Slide 6
time of E. coli growth in culture (hours)
Number
of cells
Growth of Transformed Cells in Culture

## Slide 7
Bioreactor with cells
Controller
supplying gas, acid or base etc
Computer controlling bioreactor

## Slide 8: Step 2- : Harvesting and Initial Purification Steps
Location of Product
Is it inside the cell?
Can be separated from media by centrifugation and concentrated in the cell pellet E.coli product (GFP) is kept
Is it outside the cell?
Product is in the media and is diluted
It often needs to be concentrated
Mammalian cells transport product out of cell

## Slide 9: Isolation of GFP from Transformed E. Coli
Step1 - If product is retained in cell:
Transfer all contents of media + cells into a centrifuge tube once cell growth is achieved
Place this tube plus balancing tube into centrifuge and spin at selected speed
Remove tube with cells and a pellet should present (since GFP glows, check tube with UV light to determine the location of GFP)

## Slide 10: Centrifugation and Tangential Flow Filtration (TFF)
Centrifuge
TFF process
Tangential Flow Filtration separates molecules by membrane pore size
Separates by centripetal force acting on different sized particles
rotor
Novasep.com
Glossary.periodni.com

## Slide 11: Pelleted Cells Will Glow under UV After Centrifugation
Cell pellet
Seen under UV light
media
Colony is placed into media containing penicillin and arabinose and grown
After
spinning

## Slide 12: Tangential Flow Filtration Downstream Processing
This technique allows large volumes of media to be concentrated, removal or exchange of salts in solutions etc.

## Slide 13: Lysing Cells to Release Product
Cells must be broken open to release product from the intracellular space . This can be done by the following means:
Freeze/thawing of cell pellet will break open the cell wall. (requires freezing pellet). Addition of lysozyme facilitates process
Homogenize pellet by grinding with specially designed homogenizers (is frequently used and requires less time)
Sonication will break open membranes in an efficient way

## Slide 14: Basics of Chromatography
What is it?
  Components are distributed between two phases
    Stationary phase
    Mobile phase which moves across the stationary phase
  A Physical method that gently separate mixtures
Different rates of moving over the stationary phase separates different molecules
  It is a very gentle process: does not denature proteins
  Large amounts of product can be reliably isolated
Proteins that differ by one amino acid can be separated by this method

## Slide 15: Types of Low Pressure Liquid Chromatography (LPC)
Adsorption
Ion Exchange
Molecular Size Exclusion
Affinity

## Slide 16: Adsorption Chromatography
Hydrophobic Interaction Chromatography
uses a mobile liquid or gaseous phase that becomes adsorbed to the stationary phase
differences in adsorption separate molecules

## Slide 17: Ion Exchange Chromatography
Electrostatic forces attract oppositely charged ions between molecules in mobile and the stationary phase
The strength of the attraction determines how long a molecule will stays on the resin resulting in separation

## Slide 18
Positively charged Ions do not attach to resin & pass through
Negatively charged ions attach to the column
Anion Exchange Columns and How They Work cont’d

## Slide 19: Molecular Size Exclusion Chromatography
Bead size allows only small molecules into the bead
Small molecules are last to emerge from the column
Mixtures of differently sized molecules are added to the column
Large molecules will be eluted first, smallest last
Column resin must not
be disturbed since all
sized molecules will pass through the channels
.
Siumed.edu

## Slide 20: Affinity Chromatography
Affinity Column
How it is used
1. Stationary phase has an antigen covalently attached to the fixed resin
2. A mixture containing the antibody that can recognize the antigen will attach to it non-covalently
3. The substances in the mixture not wanted are washed out from column
4. The elution step releases the antibody from the antigen on the column by high salt or low pH resulting in a pure antibody being collected from column

## Slide 21: Column Chromatography of GFP

## Slide 22: Standard Operating Procedures
You will be purifying the original mixture from GFP transformed E.coli cells using column chromatography
Harvest cells by centrifugation and add lysozyme. Place in freezer overnight
Centrifuge the treated cells after defrosting them to collect the supernatant for columns
SOP’s for each step is found in your workshop book, starting on pages

## Slide 23: Day 1-Growing Transformed Cells
1 | 

## Slide 24: Day 2
Cells must be lysed; freezing and thawing works well.

## Slide 25: HIC Columns
Some proteins are hydrophobic or water hating
High salt concentration causes protein to fold exposes hydrophobic regions to outside and proteins stick to the column
When low salt buffer is added, hydrophilic areas are exposed – protein is released

## Slide 26: Day 3

## Slide 27: Four Different Buffers for Use in Column
Equilibration buffer- 2M ammonium sulfate
Binding buffer- 4M ammonium sulfate
Wash buffer- 1.3 M ammonium sulfate
Elution buffer- low salt TE buffer

## Slide 28: Preparation of HIC

## Slide 29: Equilibration Buffer

## Slide 30: Purification Step 1
Label three collection tubes 1,2,3
Place column into tube 1 and allow liquid to run through column
Place 250 ul of supernatant onto the top of the column
Let the liquid empty from column
Move column to tube 2

## Slide 31: Purification Step 2
Add 250 ul of wash buffer to the column and allow all liquid to empty into tube 2
This allows most of the cellular proteins to be rinsed through column
GFP protein should still be attached to column

## Slide 32: Purification Step 3
Move column to test tube 3
Finally, add 750 ul of TE buffer (low binding) to
column and allow it to run completely through
into test tube 3
This buffer should elute the GFP protein

## Slide 33: Examination of test tubes
Examine all three test tubes by viewing under a UV light
Which test tubes should contain the GFP?
Compare your results with the expected ones on next slide
Secure all your column fractions needed for SDS PAGE analysis