## Slide 1: Downstream Processing

## Slide 2: Know the Characteristics of Your Protein Green Fluorescent Protein (GFP)
Sequence of Amino Acids
MSKGEELFTGVVPVLVELDGDVNGQKFSVSGEGEGDATYGKLTLNFICTTGKLPVPWPTLVTTFSYGVQCFSRYPDHMKQHDFFKSAMPEGYVQERTIFYKDDGNYKTRAEVKFEGDTLVNRIELKGIDFKEDGNILGHKMEYNYNSHNVYIMGDKPKNGIKVNFKIRHNIKDGSVQLADHYQQNTPIGDGPVLLPDNHYLSTQSALSKDPNEKRDHMILLEFVTAARITHGMDELYK
Tertiary Structure

## Slide 3: Green Fluorescent Protein (GFP)
MW (molecular weight = 27,000 Daltons (27 kD)
pI (isoelectric point) - 4.8
Hydropathicity (hydrophobicity) - hydrophobic amino acids make up GFP’s fluorophore; amino acids associated with the fluorophore are also hydrophobic

## Slide 4
GFP Chromatophore - Hydrophobic

## Slide 5: Downstream Processing in Biopharmaceutical Manufacturing
Protein Purification
Harvest by Centrifugation
Clarification by Depth Filtration
Sterile Filtration (MF)
Tangential Flow Filtration (UF/DF)
Low Pressure Liquid Column Chromatography
Notes: MF=microfiltration with .1 to .22u (pore size) filters
UF=ultrafiltration with e.g. 10,000Dalton (pore size) cut-off filters
DF=diafiltration where you exchange buffers and/or concentrate protein of interest

## Slide 6
Media Prep
Working Cell
Bank
Sub-
Culture
Inoculum
Sub-
Culture
Sub-
Culture
Sub-
Culture
Sub-
Culture
Large Scale Bioreactor
Wave
Bag
Seed Bioreactors
Fermentation
150L Bioreactor
750L Bioreactor
5,000L Bioreactor
26,000L Bioreactor
Depth
Filtration
Collection
Centrifuge
Harvest/Recovery
Harvest
Collection
Tank
1,500L
Filter
Chromatography Skid
Anion Exchange Chromatography (QXL)
Column
Eluate
Hold
Tank
8,000L
Eluate
Hold
Tank
6,000L
Filter
Chromatography Skid
Protein A Chromatography
Column
Chromatography Skid
Column
Eluate
Hold
Tank
20,000L
Hydrophobic Interaction Chromatography (HIC)
Eluate
Hold
Tank
20,000L
Viral Inactivation
Eluate
Hold
Tank
5,000L
Filter
Chromatography Skid
Anion Exchange Chromatography (QFF - Fast Flow)
Column
Post-viral
Hold
Vessel
3,000L
Viral Filtering
Ultra Filtration
Diafiltration
Bulk Fill
Purification
24 days
31 days
8 days
1 day

## Slide 7: Protein Purification - Filtration
Separate protein using pores in solid media - small pore excludes large proteins (and vice versa):
Depth Filtration
Tangential Flow Filtration
Ultrafiltration
Sterile Filtration
Defiltration

## Slide 8: Protein Purification – Liquid Chromatography
Separate protein using different affinities for a solid media (matrix or bead) vs. liquid buffer:
Hydrophobic Interaction Chromatography (HIC)
Ion Exchange Chromatography (IEX):
  Anion Exchange Chromatography
  Cation Exchange Chromatography
Affinity Chromatography
Gel Filtration or Size Exclusion Chromatography

## Slide 9: Methods to Remove Cells and Cellular Debris
Centrifugation
Depth Filtration

## Slide 10: Centrifuge

## Slide 11: Depth Filtration
Cells and cellular debris stick to ceramic encrusted fibers in pads

## Slide 12: Tangential Flow Filtration- TFF
Used to separate of protein of interest
Using TFF with the right cut off filters, the protein of interest can be separated from other proteins and molecules in the sterile filtered, clarified medium
  e.g HSA has a molecular weight of 69KD . To make sure that the protein of interest is retained, a 10KD cut-off filter is used
After ultrafiltration perform defiltration with buffer used to prepare for affinity chromatography of HSA

## Slide 13: How TFF Concentrates and Purifies a Protein of Interest

## Slide 14: Low Pressure Liquid (Production) Chromatography
The Media:
Hydrophobic Interaction (HIC)
Ion Exchange (Anion AEX and Cation CEX Exchange)
Gel Filtration (=Size Exclusion)
Affinity
The System: Components and Processes

## Slide 15: Hydrophobic Interaction Chromatography (HIC
HIC media have high capacity and are economical and stable; capable of powerful resolution
used in therapeutic antibody purification because part antibodies are found in membranes, are lipid soluble and therefore hydrophobic
molecular mechanism relies on unique structural features- serves as an orthogonal method to ion exchange and affinity chromatography
adsorption takes place in high salt and elution in low salt concentrations These special properties make HIC very useful in whole processes for bridging or transitioning between other steps in addition to the separation which is effected

## Slide 16: Ion Exchange Chromatography
Separates by Charge

## Slide 17: Isoelectric Focusing or IEF
If the pI of your protein (or the pH at which your protein is neutral) is known , you can place it in a buffer at a lower or higher pH to alter its charge
If the pH of the buffer < pI, the protein of interest will become positively charged
If the pH of the buffer > the pI, the protein of interest will become negatively charged

## Slide 18: Liquid Column Chromatography Process
PURGE Air from Column use Equilibration Buffer
PACK Column with Beads (e.g. ion exchange, HIC, affinity or gel filtration beads/media)
EQUILIBRATE Column with Equilibration Buffer
LOAD Column with Protein of Interest in Equilibration Buffer
WASH Column with Equilibration Buffer
ELUTE Protein of Interest with Elution Buffer of High or Low Salt or pH
REGENERATE Column or Clean and Store (NaOH)

## Slide 19: Liquid Column Chromatography

## Slide 20: GFP Chromatography (HIC)
GFP moving through HIC column
Notes: GFP band or peak moving through HIC column.

## Slide 21: GFP Chromatography
Droplet of GFP
Notes: Droplet of GFP caught in ‘fraction collector’.

## Slide 22: LP LC System Components
Mixer for Buffers, Filtrate with Protein of Interest, Cleaning Solutions
Peristaltic Pump
Chromatography Column and Media (Beads)
Conductivity Meter
UV Detector

## Slide 23: LP LC System Components- Peristaltic Pump
Creates a gentle squeezing action to move fluid through flexible tubing

## Slide 24: LC System Components
UV Detector - detects proteins from the column by measuring absorbance at 280nm
Conductivity Meter - measures the amount of salt in the buffers coming out of the columns – high salt or low salt are often used to elute the protein of interest from the chromatography beads

## Slide 25: Height Equivalent to Theoretical Plate (HETP)
HETP = L/N
  L=length of column in mm
  N=column efficiency
allows comparison of columns of different lengths
smaller the HETP the better
shorter the column the better

## Slide 26: Calculating Column Efficiency (N)

## Slide 27: A Typical Chromatogram
Flow
Through
Eluate
Wash
Notes: If you were running HIC columns, the chromatogram produced would show flow through of (hydrophilic) proteins that do not attach to the HIC column, no proteins in the wash, followed by a peak of hydrophobic GFP eluted from the HIC column with low salt.