## Slide 1: Downstream Processing

## Slide 2: Know the Characteristics of Your Protein Green Fluorescent Protein (GFP)
Sequence of Amino Acids
MSKGEELFTGVVPVLVELDGDVNGQKFSVSGEGEGDATYGKLTLNFICTTGKLPVPWPTLVTTFSYGVQCFSRYPDHMKQHDFFKSAMPEGYVQERTIFYKDDGNYKTRAEVKFEGDTLVNRIELKGIDFKEDGNILGHKMEYNYNSHNVYIMGDKPKNGIKVNFKIRHNIKDGSVQLADHYQQNTPIGDGPVLLPDNHYLSTQSALSKDPNEKRDHMILLEFVTAARITHGMDELYK
Tertiary Structure

## Slide 3: Know the Characteristics of Your Protein Green Fluorescent Protein (GFP)
MW (molecular weight = 27,000 Daltons (27 kD)
pI (isoelectric point) = 4.8
Hydropathicity (=hydrophobicity) = hydrophobic amino acids make up GFP’s fluorophore; amino acids associated with the fluorophore are also hydrophobic

## Slide 4
GFP Chromatophore - Hydrophobic

## Slide 5: Downstream Processing in Biopharmaceutical Manufacturing
Harvest by Centrifugation
Clarification by Depth Filtration
Sterile Filtration (MF)
Tangential Flow Filtration (UF/DF)
Low Pressure Liquid Column Chromatography
Protein Purification
Notes: MF=microfiltration with .1 to .22u (pore size) filters
UF=ultrafiltration with e.g. 10,000Dalton (pore size) cut-off filters
DF=diafiltration where you exchange buffers and/or concentrate protein of interest

## Slide 6: Protein Purification Methodology
FILTRATION
Separate protein using pores in solid media - small pore excludes large proteins (and vice versa):
Normal Filtraton
Depth Filtration
Tangential Flow Filtration
Ultrafiltration
Sterile Filtration
Diafiltration
Gel Filtration=Size Exclusion
LIQUID CHROMATOGRAPHY
Separate protein using different affinities for a solid media (matrix or bead) vs. liquid buffer:
Hydrophobic Interaction Chromatography (HIC)
Ion Exchange Chromatography (IEX):
  Anion Exchange Chromatography
  Cation Exchange Chromatography
Affinity Chromatography
Gel Filtration or Size Exclusion Chromatography

## Slide 7
Media Prep
Working Cell
Bank
Sub-
Culture
Inoculum
Sub-
Culture
Sub-
Culture
Sub-
Culture
Sub-
Culture
Large Scale Bioreactor
Wave
Bag
Seed Bioreactors
Fermentation
150L Bioreactor
750L Bioreactor
5,000L Bioreactor
26,000L Bioreactor
Depth
Filtration
Collection
Centrifuge
Harvest/Recovery
Harvest
Collection
Tank
1,500L
Filter
Chromatography Skid
Anion Exchange Chromatography (QXL)
Column
Eluate
Hold
Tank
8,000L
Eluate
Hold
Tank
6,000L
Filter
Chromatography Skid
Protein A Chromatography
Column
Chromatography Skid
Column
Eluate
Hold
Tank
20,000L
Hydrophobic Interaction Chromatography (HIC)
Eluate
Hold
Tank
20,000L
Viral Inactivation
Eluate
Hold
Tank
5,000L
Filter
Chromatography Skid
Anion Exchange Chromatography (QFF - Fast Flow)
Column
Post-viral
Hold
Vessel
3,000L
Viral Filtering
Ultra Filtration
Diafiltration
Bulk Fill
Purification
24 days
31 days
8 days
1 day
Upstream/Downstream Manufacturing EXAMPLE

## Slide 8: Clarification or Removal of Cells and Cell Debris
Using Centrifugation
Using Depth Filtration

## Slide 9: Centrifuge
Control Panel
Cut-away view
Protective enclosure
Basic components of a centrifuge
Door
Rotor
Drive
shaft
Motor
Centrifugal force
Sedimentation
path of particles
Pellet deposited
at an angle
Center of rotation
rminimum
raverage
rmaximum
An instrument that generates centrifugal force.
Commonly used to separate particles in a liquid from the liquid.
Notes: An instrument that generates centrifugal force.
Commonly used to separate particles in a liquid
from the liquid

## Slide 10
Industrial Continuous Centrifuge
Media and Cells In & Clarified Media Out
Notes: Continuous multichamber disc-stack centrifuge. The bowl contains a
number of parallel discs providing a large clarifying surface with a small sedimentation distance. The sludge (cells) is removed through

## Slide 11
Sludge
Continuous
Centrifuge
Cells + Media In
Media Out

## Slide 12: More Details on Continuous Centrifugation
Continuous Centrifuge
Manifold for Mechanical
Routing of Fluids
Centrifuge
Motor

## Slide 13: Depth Filtration Equipment

## Slide 14: Depth Filtration: Cells and Cellular Debris Stick to Ceramic Encrusted Fibers in Pads
PROTEIN of INTEREST

## Slide 15
Depth Filter Housings and Filters

## Slide 16
Sterile Filters
Notes: Sterile filters are filled with tightly wound material containing .1 to .2u pores. Harvested, clarified media from the bioreactor is forced down through the middle of the sterile filter; the media moves radially through the filter trapping any particles, including microbes and then down the sides and out stainless steel piping to a hold tank for further purification by chromatography and filtration.

## Slide 17: Tangential Flow Filtration – TFF Separation of Protein of Interest
Using TFF with the right cut off filters, the protein of interest can be separated from other proteins and molecules in the sterile filtered, clarified medium.
For instance HSA has a molecular weight of 69KD. To make sure that the protein of interest is retained, a 10KD cut-off filter is used.
After ultrafiltration, we can diafilter, adding the phosphate buffer at pH 7.1 that we will also use to equilibrate our affinity column to prepare it for affinity chromatography of HSA.

## Slide 18: How TFF Concentrates and Purifies a Protein of Interest

## Slide 19: Downstream Processing Equipment
Lab-Scale TFF System
Large-Scale TFF System

## Slide 20: Low Pressure Liquid (Production) Chromatography
The Media:
Hydrophobic Interaction (HIC)
Ion Exchange (Anion AEX and Cation CEX Exchange)
Gel Filtration (=Size Exclusion)
Affinity
The System: Components and Processes

## Slide 21: Hydrophobic Interaction Chromatography (HIC)
HIC is finding dramatically increased use in production chromatography. Since the molecular mechanism of HIC relies on unique structural features, it serves as an orthogonal method to ion exchange and affinity chromatography. It is very generic, yet capable of powerful resolution. Usually HIC media have high capacity and are economical and stable. Adsorption takes place in high salt and elution in low salt concentrations. These special properties make HIC very useful in whole processes for bridging or transitioning between other steps in addition to the separation which is effected.
Used in therapeutic antibody purification because part antibodies are found in membranes, are lipid soluble and therefore hydrophobic.

## Slide 22: Ion Exchange Chromatography Separates by Charge
.

## Slide 23: Isoelectric Focusing or IEF
Once you know the pI of your protein (or the pH at which your protein is neutral), you can place it in a buffer at a lower or higher pH to alter its charge. If the pH of the buffer is less than the pI, the protein of interest will become positively charged. If the pH of the buffer is greater than the pI, the protein of interest will become negatively charged.
pH < pI < pH
+ 0 -

## Slide 24: GFP Ion Exchage Separation Strategy
GFP has a pI of 4.8
The E.coli supernatate containing GFP is put into pH 8.3 buffer, giving it a negative charge.
GFP will stick to the positively charged AEX beads. It will be eluted with high salt.
GFP will not be attracted to the negatively charged CEX beads and will be found in the flow through. Positively charged proteins will attatch to the beads and will be eluted with high salt.

## Slide 25: Liquid Column Chromatography Process
PURGE Air from Column use Equilibration Buffer
PACK Column with Beads (e.g. ion exchange, HIC, affinity or gel filtration beads/media)
EQUILIBRATE Column with Equilibration Buffer
LOAD Column with Protein of Interest in Equilibration Buffer
WASH Column with Equilibration Buffer
ELUTE Protein of Interest with Elution Buffer of High or Low Salt or pH
REGENERATE Column or Clean and Store (NaOH)
Notes: The processes in red will be carried out today (Day 3) in small plastic columns packed with beads

## Slide 26: Liquid Column Chromatography

## Slide 27: GFP Chromatography (HIC)
GFP moving through HIC column
Notes: GFP band or peak moving through HIC column.

## Slide 28: GFP Chromatography
Droplet of GFP
Notes: Droplet of GFP caught in ‘fraction collector’.

## Slide 29: A Typical Chromatogram
Flow
Through
Eluate
Wash
Notes: If you were running HIC columns, the chromatogram produced would show flow through of (hydrophilic) proteins that do not attach to the HIC column, no proteins in the wash, followed by a peak of hydrophobic GFP eluted from the HIC column with low salt.

## Slide 30
Component | Culture Harvest Level | Final Product Level | Conventional Method
Therapeutic Antibody | 0.1-1.5 g/l | 1-10 g/l | UF/Cromatography
Isoforms | Various | Monomer | Chromatography
Serum and host proteins | 0.1-3.0 g/l | < 0.1-10 mg/l | Chromatography
Cell debris and colloids | 106/ml | None | MF (Depth Filtration)
Bacterial pathogens | Various | <10-6/dose | MF (Sterile Filtration)
Virus pathogens | Various | <10-6/dose (12 LRV) | virus filtration
DNA | 1 mg/l | 10 ng/dose | Chromatography
Endotoxins | Various | <0.25 EU/ml | Chromatography
Lipids, surfactants | 0-1 g/l | <0.1-10 mg/l | Chromatography
Buffer | Growth media | Stability media | UF
Extractables/leachables | Various | <0.1-10 mg/l | UF/ Chromatography
Purification reagents | Various | <0.1-10mg/l | UF
Common Process Compounds and Methods of Removal or Purification*

## Slide 31: GFP Product in Glass Heart

## Slide 32: LP LC System Components
Mixer for Buffers, Filtrate with Protein of Interest, Cleaning Solutions
Peristaltic Pump
Chromatography Column and Media (Beads)
Conductivity Meter
UV Detector

## Slide 33: Peristaltic Pump
Creates a gentle squeezing action to move fluid through flexible tubing.
Notes: Creates a gentle squeezing action to move fluid through flexible tubing.
In this example three rollers on rotating arms pinch the tube against an arc and move the fluid along. There are usually three or four sets of rollers

## Slide 34: UV Detector
Detects proteins coming out of the column by measuring absorbance at 280nm

## Slide 35: Conductivity Meter
Measures the amount of salt in the buffers coming out of the columns – high salt or low salt are often used to elute the protein of interest from the chromatography beads.

## Slide 36
Virtual Chromatography – The Power of Interactive Visualization in Understanding a STEM Field of Study
Understanding the physics, chemistry and biology of the chromatographic system and the binding of the protein of interest to the chromatographic matrix or beads (Science)
Understanding the design and operation of chromatography components and of the chromatographic process (Technology and Engineering).
Understanding the calculations needed to run the chromatographic system (column volume) and the measurements on chromatograms needed to calculate the HETP, number of theoretical plates, retention time, and resolution (Mathematics).

## Slide 37
Actual BioLogic System
Complex System
Not easy to ‘see’ interaction of components
Students use virtual system to prepare to use actual system
Use virtual system for BIOMANonline
System same as industrial chromatography skid

## Slide 38
Conductivity Meter
UV Detector
Mixer
Peristaltic
Pump
Column
Injector Valve
Buffer Select

## Slide 39: Virtual Chromatography – Components Engineering and Advanced Technology
A screenshot of the Virtual Liquid Chromatography Laboratory.
3D images of major system components are delivered as you click on them.

## Slide 40: Virtual Chromatography – Controller Engineering and Advanced Technology
The Virtual Liquid Chromatography Laboratory showing the interactive controller which
enables students to operate the system and set process parameters.

## Slide 41: Virtual Chromatography - Chromatogram with Mathematics
The Virtual Chromatography Laboratory teaches students how to make calculations on chromatograms such as the efficiency of column packing (HETP).

## Slide 42: Height Equivalent to Theoretical Plate (HETP)
The smaller the HETP the better
Shorter the column the better
Allows comparison of columns of different lengths
Column length expressed in mm
HETP = L/N
L=length of column in mm
N=column efficiency

## Slide 43: Calculating Column Efficiency (N)
tR
w1/2
N = 5.54 (tR/w1/2)2
Notes: Load a very small volume (~1% CV) of non-interacting molecule, e.g. for ion exchange load column load 1% CV of 0.8M NaCl and measure conductivity peak.
Measurements for determining the HETP are made on the peak of the chromatogram; use the following equation to determine the HETP:
Taller columns will have higher N compared to shorter columns because retention time will be greater.

## Slide 44: Virtual Chromatography – Chromatography Science and Technology
The Virtual Chromatography Laboratory showing the operation of the chromatography system during the ‘load’ phase, the chromatogram showing the flow through of proteins that do not attach to the chromatographic matrix, and a nanoscale view inside the column of the affinity bead with the protein of interest in the filtrate (green) attached and proteins not specific for the bead flowing through the column.

## Slide 45: Virtual Chromatography – Chromatography Science and Technology
The Virtual Chromatography Laboratory showing the operation of the chromatography system during the ‘elution’ phase, the chromatogram showing the beginning of the peak of the protein of interest, and a nanoscale view inside the column of the affinity bead showing the protein of interest detaching from the bead as the elution buffer (red) moves through the column.

## Slide 46: The Virtual Chromatography Laboratory
URL: http://ATeLearning.com/BioChrom/
To login enter your email address and the password: teachbio

## Slide 47: Downstream Processing Equipment
Lab Scale (1 cm diameter)
Chromatography System
Industrial Scale (90 cm diameter)
Chromatography System

## Slide 48: Protein is Cash Course in a Box
Protein is Cash - Day 3: Downstream Processing
Items | Source | Amount | Cost
SOP: Protein is Cash Day 3 Downstream Processing | NBC2 | 20 each | $ 5.00
KIT: GFP Chromatography Kit | Bio-Rad | 1 each | $89.00
Equipment Mini-Centrifuge Microtube rack Eppendorf Tubes (2ml) | Bio-Rad NBC2 NBC2 | 5 each 10 each 1 bag (150) | 
Supplies E. coli - GFP transformed AEX Columns CEX Columns IEX Equilibration Buffer IEX Elution Buffer 1 IEX Elution Buffer 2 GFP Standard UV Pen Lights Glass Hearts |  | 1 ml cryovial 10 each 10 each 10 ml 10 each 20 each | $33.00
Virtual Downstream Processing Module CD Thumb Drive App Subscription |  |  | 
Draft Concept
Notes: This is an example of materials we could offer through an e-Store.